## Slide 1: Cyber Forensics
Unit 1.3 – Cell Phone and Mobile Device Forensics

## Slide 2: Cell Phone and Mobile Device Forensics
People store a wealth of information on cell phones and smart phones, and the thought of losing your phone and, therefore, the information stored on it can be a frightening prospect.
Despite this concern, not many people think about securing their phones
Many people store more information on phones than on computers
Telecommunications Industry Association (TIA), these systems are referred to as CDMAOne, and when they went to 3G services, they became CDMA2000.

## Slide 3
Global System for Mobile Communications (GSM) uses the Time Division Multiple Access (TDMA) technique, so multiple phones take turns sharing a channel on a round-robin basis.
The 3G standard was developed by the International Telecommunication Union (ITU) under the United Nations. It’s compatible with CDMA, GSM, and TDMA.
The Enhanced Data GSM Environment (EDGE) standard was developed specifically for 3G.

## Slide 4: 4G networks can use the following technologies:
Orthogonal Frequency Division Multiplexing—The Orthogonal Frequency Division
Multiplexing (OFDM) technology uses numerous parallel carriers instead of a single broad carrier and is less susceptible to interference
Mobile WiMAX—This technology uses the IEEE 802.16e standard and Orthogonal Frequency Division Multiple Access (OFDMA) and supports transmission speeds of 12 Mbps. Sprint, an American Telecommunication company, chose this technology for its 4G network, although some argue it’s not true 4G.
Ultra Mobile Broadband (UMB)—Also known as CDMA2000 EV-DO, this technology was used by CDMA network providers to switch to 4G and supports transmission speeds of 275 Mbps for downlinks and 75 Mbps for uplinks.
Multiple Input Multiple Output (MIMO)—This technology, developed by Airgo and acquired by Qualcomm(a wireless technology), supports transmission speeds of 312 Mbps and is used by 4G, WiMAX, and other technologies.

## Slide 5: three main components are used for communication with different geographical areas:
• Base transceiver station (BTS)—This component is made up of radio transceiver equipment that defines cells and communicates with mobile phones; it’s sometimes referred to as a “cell phone tower,” although the tower is only one part of the BTS equipment.
• Base station controller (BSC)—This combination of hardware and software manages BTSs and assigns channels by connecting to the mobile switching center.
• Mobile switching center (MSC)—This component connects calls by routing digital packets for the network and relies on a database to support subscribers. This central database contains account data, location data, and other key information needed during an investigation. If you have to retrieve information from a carrier’s central database, you usually need a warrant or subpoena.

## Slide 6: Inside Mobile Devices
Phones store system data in electronically erasable programmable read-only memory (EEPROM), which enables service providers to reprogram phones without having to access memory chips physically.
Many users take advantage of this capability by reprogramming their phones to add features or switch to different service providers.
The OS is stored in ROM, which is nonvolatile memory, so along with other data, it’s available even if the phone loses power.
PDAs house a microprocessor, flash ROM, RAM, and other hardware components.
As with smartphones, the amount of information on a PDA varies depending on the model.

## Slide 7: A number of peripheral memory cards are used with PDAs:
• Compact Flash (CF)—CF cards were used for extra storage and work much the same way as PCMCIA cards.
• MultiMediaCard (MMC)—MMC cards were designed for mobile phones, but they can be used with PDAs to provide another storage area.
• Secure Digital (SD)—SD cards are similar to MMCs but have added security features to protect data; they’re now used on smartphones.

## Slide 8: SIM Cards
Subscriber identity module (SIM) cards are usually found in GSM devices and consist of a microprocessor and internal memory.
SIM cards are similar to standard memory cards, except the connectors are aligned differently.
GSM refers to mobile phones as “mobile stations” and divides a station into two parts: the SIM card and the mobile equipment (ME), which is the remainder of the phone.
The SIM card is necessary for the ME to work and serves these additional purposes:
• Identifies the subscriber to the network
• Stores service-related information
• Can be used to back up the device

## Slide 9: Acquisition Procedures for Cell Phones and Mobile Devices
All mobile devices have volatile memory, so making sure they don’t lose power before you can retrieve RAM data is critical.
At the investigation scene, determine whether the device is on or off.
Note this step in your log if you can’t determine whether the device was charged at the time of seizure
mobile devices are often designed to synchronize with applications
mobile device attached to a PC or tablet via a USB cable or micro USB cable should be disconnected immediately

## Slide 10
Disconnect the devices from Internet immediately helps prevent synchronization that might occur automatically on a preset schedule and overwrite data on the device
determine whether the hard drive contains any information that’s been transferred and then deleted from the mobile device, including pictures, videos, and other files that have been transferred and then deleted.
If you determine that the device should be turned off to preserve battery power or a possible attack, note the time and date at which you take this step.
When you’re back in the forensics lab, you need to assess what can be retrieved.
To determine whether you should do a logical acquisition or physical acquisition, you need to know where information is stored.

## Slide 11
You should check the following locations for information
Internal memory
SIM card
Removable or external memory cards
Network provider
You can retrieve quite a bit of data from a SIM card, depending on whether the phone is GSM or CDMA.
The information that can be retrieved falls into four categories:
• Service-related data, such as identifiers for the SIM card and subscriber
• Call data, such as numbers dialed
• Message information
• Location information

## Slide 12
Memory storage on a mobile device is usually a combination of volatile and nonvolatile memory. Volatile memory requires power to maintain its contents, but nonvolatile memory doesn’t.
Although the locations of data vary from one phone model to the next, volatile memory usually contains data that changes frequently, such as missed calls, text messages, and sometimes even user files.
Nonvolatile memory, on the other hand, contains OS files and stored user data, such as a personal information manager (PIM) and backed-up files.